Bluetooth waveforms for the HP ESG-D and ESG-DP Series

These files provide various Bluetooth waveforms, some of which are specified by revision 0.31 of the Bluetooth RF Test Specification. More information about this wireless communications standard can be found at http://www.bluetooth.com/.

Files:

Each of the following waveform file pairs generate a single Bluetooth compliant GFSK modulated TDD burst repeated at an appropriate multiple (x1, x2 or x3) of the frame period (1.25ms).  The modulated data is fully structured and encoded according to the Bluetooth Core Specification Version 1.0.  However, as these are pre-compiled arbitrary waveform files, the implementation of certain dynamic aspects of the encoding process, such as data whitening and payload flow control flags is necessarily limited.

* Files in this archive are preceded by "rev-B"

I                  	Q

366 bits :  Access code / Header / PN9 payload			dh1i.asc		dh1q.asc

1622 bits: Access code / Header / PN9 payload			dh3i.asc		dh3q.asc

2870 bits: Access code / Header / PN9 payload			dh5i.asc		dh5q.asc

366 bits :  Access code / Header / PN9 payload (2/3 FEC)		dm1i.asc		dm1q.asc

1626 bits: Access code / Header / PN9 payload (2/3 FEC)		dm3i.asc		dm3q.asc

2871 bits: Access code / Header / PN9 payload (2/3 FEC)		dm5i.asc		dm5q.asc

356 bits: Access code / Header / PN9 data / PN9 voice (2/3 FEC)	dvi.asc		dvq.asc

294 bits: Header / FHS payload (2/3 FEC)				fhsi.asc		fhsq.asc

366 bits: Access code / Header / PN9 payload (1/3 FEC)		hv1i.asc		hv1q.asc

366 bits: Access code / Header / PN9 payload (2/3 FEC)		hv2i.asc		hv2q.asc

366 bits: Access code / Header / PN9 payload			hv3i.asc		hv3q.asc

126 bits: Access code / Header					nulli.asc		nullq.asc

All the above normal packet waveforms were generated with the following parameters,

Bluetooth Master Device Address = 8

Bluetooth Slave Device Address = 1

Bluetooth Master Clock = static at 123456789h (hex)

Data Whitening ON

Peak Deviation = 157.5 kHz

In addition to the standard waveforms listed above, there are some "special" files which may prove useful for receiver testing,

DH1, 25kHz drift, 157.5 kHz deviation, PN payload			dh1d25ki.asc 	dh1d25kq.asc

DH5, 40kHz drift, 157.5 kHz deviation, PN payload 			dh5d40ki.asc 	dh5d40kq.asc

DH1, 175 kHz deviation, PN payload 				dh1maxdi.asc 	dh1maxdq.asc

DH1, 140 kHz deviation, PN payload 				dh1mindi.asc 	dh1mindq.asc

00001111 repeat, 25kHz drift, 157.5 kHz deviation 			alt4d25ki.asc 	alt4d25kq.asc

00001111 repeat, 175 kHz deviation 				alt4maxdi.asc 	alt4maxdq.asc

00001111 repeat, 140 kHz deviation 				alt4mindi.asc 	alt4mindq.asc

The ESG arb setup parameters for all the above signals are:

Clock frequency: 10 MHz

Reconstruction filter: 2.5 MHz

Notes:

(1) Used in section 2.1.4 Modulation Characteristics of the Bluetooth transmitter.

Platforms:

Windows 95, Windows NT

Interface:

Use the Windows1-based download utility available at http://www.hp.com/go/esg/ to download these waveform files to an HP ESG-D series signal generator with Option UND, internal dual arbitrary waveform generator.

Instructions for Downloading Software and Waveform Files

Create a directory on your hard drive for the file (*.exe). Activate the hyperlink to the software or waveform file. When the download window appears, type in the appropriate path to the directory you created on your hard drive, and press the save button.

Windows 3.x or Windows for Workgroups 3.111 
Start Windows File Manager. Choose "File" from File Manager's menu bar, select the "Run" option, specify the path and filename, and press okay. This will unpack the self-extracting archive into your directory. Follow the instructions in readme.txt for installing software and waveforms.

Windows 95 or Windows NT1 
Click the "Start" button and choose the "Run" option. Specify the path and filename, and press okay. This will unpack the self-extracting archive into your directory. Follow the instructions in readme.txt for installing software and waveforms.

1Windows® Windows 95®, and Windows NT® are U.S. registered trademarks of Microsoft Corporation.

Revision history:

September 22, 1999 - These files have the HEC/CRC bug fixed.

May 1, 2000 - Rev-B; Fixed error in HEC and CRC generators.